## Slide 1: Stream Processes and Habitat
Ryan Johnson

## Slide 2: Overview
Watershed Processes
  Factors and their effects on the watershed as a whole
Stream Processes
  Factors controlling individual stream dynamics
Stream Habitat
  How these processes affect local wildlife

## Slide 3: Watershed Processes

## Slide 4: Factors
Climate & Geology
  Control ecosystem components
Three basic components
  Soil
  Vegetation
  Water

## Slide 5: Soil
Stores and provides water for stream
  Primary source of streamflow
Storage factors
  Depth & Texture
Delivery rate factors
  Slope, Texture, and Structure

## Slide 6: Vegetation
Provides resistance to erosion throughout watershed
Prevents oversaturation of soil
Protects from splash erosion

## Slide 7: Water
How much water is the watershed receiving?
  Climate
  Time of year

## Slide 8: Land Use
If human activity substantially differs from natural disturbance regime:
  Causes substantial alteration
Any alteration of three basic components will affect the watershed
  Removal of vegetation (farming/logging)
  Compaction of soil (road building)
  Diversion of water (irrigation)
  Alterations tend to accelerate over time

## Slide 9: Disturbances
Ecosystems evolve according to disturbance cycle
  i.e. floods
Large & small scale
  Critical to function of ecosystem
  Resets the ‘successional clock’
  Creates complexity in ecosystem

## Slide 10: Healthy vegetative community = Healthy watershed function

## Slide 11: What does it all mean?
If alterations of the watershed go beyond the system’s ability to resist or recover from them, ecosystem degradation will occur.
At that point, restoration efforts are required to stimulate recovery of the watershed.

## Slide 12: River Processes

## Slide 13: What does a river want to do?
Adjust towards an equilibrium
Balance of energy in and energy out
Balance of deposition and erosion

## Slide 14: Factors
What determines stream morphology?
  Energy
  Water
  Sediment
  Structural Elements

## Slide 15: River Types
Non-alluvial
  Controlled by bedrock
  Very stable and resistant to change
    Not our concern
Alluvial
  Controlled by sediment stored by river
  Presence of floodplains
  Likes to ‘misbehave’

## Slide 16: River Forms
Single Channel
  Straight or meandering
Braided Stream
  Frequent avulsion
  Stable, vegetated islands or unstable bars
  Caused by:
    Steep Gradient
    Abundant coarse bedload and/or wood supply

## Slide 17: Stream Dynamics
Gravity Energy
A stream must disperse this energy:
  Friction within channel
    Bank stability from vegetation
  Turbulence from channel form
  Sediment transport
Balanced flow & sediment load
  Creates a complex, and unique, channel geometry

## Slide 18: Flooding
A way to relieve excess energy from the stream system
Restricting flood flows (via dikes or dredging) forces energy to be contained in the stream channel
  Excess erosion and stream degradation will occur

## Slide 19: Avulsion
A natural process that can be accelerated by human activity
Chute-cutoff is most common
  Cuts off meanders that can’t effectively transport sediment
  Creates oxbow lakes
Energy of flood flow > resistance of floodplain
  Devegetation & decreased channel capacity

## Slide 20: Hyporheic Zone
Area where ground & surface water mix
  Effective in coarse-grained sediment and sufficient stream gradient
  Increase in fine-grained sediment can seal pores
Downwelling & Upwelling Zone
  Water table below or above stream
  Severe downwelling can’t support riparian vegetation

## Slide 21: Large Wood
Captures and retains sediment
Lowers stream gradient
Protects the bank from erosion
General dispersion of stream energy
Removal from stream can lead to quick erosion of bed down to bedrock
  One of the most destructive practices
In arid regions, beaver dams can serve the same purpose

## Slide 22: Disturbances
Serves similar purpose as on watersheds
Potential to mechanically alter stream channels
Stream must undergo period of recovery
  Reestablish equilibrium

## Slide 23: Threshold of Stability
Until reached:
  Small changes cause small responses by the system
Once reached:
  Small changes cause major changes in the system
Good indicator of stream degradation

## Slide 24: Degradation
Generally ‘plain’ morphology and methods of energy dissipation
  High surface resistance with excessive erosion/deposition
Unbalanced sediment transport
  Channel downcutting

## Slide 25: Stream Habitat

## Slide 26: Connectivity
Some species need to migrate
Continuous habitat and migration corridors are essential
Loss of connectivity due to degradation often results in local extinction

## Slide 27: Diversity
Lots of features = biotic diversity
  Covers needs of many species
Frequency and magnitude of floods primary driver of complexity
Moderate levels of disturbances
  Maintains complex habitat
  Allows coexistence of species with superior competitors