## Slide 1: Elk Creek Wood Replacement Phase Two Oregon Watershed Enhancement Board, 2009
Katie Halvorson

## Slide 2: Stream/site data:
1.5mile reach
Stream gradient = 1.2%
Average bankfull = 30-35feet wide
No large log jams
Watershed above project is 5miles squared

## Slide 3: Goals:
Improve stream complexity
Enhance watershed function
Increase number of pools
Increase number of juvenile coho through pools

## Slide 5: Problems with site:
Lacking large wood conditions
Total volume of wood = 11.5 meters cubed per 100meters
  ODFW says undesirable

## Slide 6: Importance of wood in watershed:
Pool scour
Sediment retention
High-quality spawning habitat
Increases stream elevation to connect channel with floodplain
Nutrient cycle processes

## Slide 7: Why no wood at this site now?
Mainly caused by intentional removal
Riparian stands going from mixed to hardwood dominated
Removal of conifers from slide draws

## Slide 8: What they did:
Constructed 16 large wood structures
  used 52 trees and logs
Root wads added
  Helps increase habitat complexity
  Aids pool scour
  Acts as anchor
All wood meet standards for permit

## Slide 9: Site conclusions:
Coho, trout, and steelhead dropped
Total length and average pool depth stayed the same
Important to check high water flows

## Slide 10: Cowan and Sinko Wetland Restoration Monitoring Baker and Miranda, 2006

## Slide 11: Objectives:
Monitor project effectiveness centered on juvenile salmon habitat use and passage capability.

## Slide 12: Cowen and Sinko wetlands

## Slide 13: Cowen wetland facts:
Project completed fall of 2002
Restored 80 acres
Mouth of Larson Slough
Chinook, Coho, and steelhead present

## Slide 14: Cowen wetland reconstruction:
Pool-weir-chute ladder installed
Controls water elevation
Allows fish into and out of wetland

## Slide 15: Sinko wetland project:
Completed summer of 2004
Restored 200 acres that was once dairy cattle pasture

## Slide 16: What they did at Sinko:
Filling drainage ditches
Restoring sinuous channels
Plating woody vegetation
Installing half-round riser water control structure

## Slide 17: Fish and Cowen
Two-way vertical slot trap was put at the entrance of fish ladder

## Slide 18: Fish and Sinko
Box trap was used to catch fish that out through water-control structure

## Slide 19: Results:
Juvenile coho were found at both sites after completion.
Coho was greater

## Slide 20: In conclusion:
Some projects will get results faster than others. It takes time for the watershed to adjust to the projects.