## Slide 1: Channel Modification and Restoration
Esteban Quiles
Earth and Physical Science Department
Western Oregon University
Monmouth, Oregon
Email: equiles12@wou.edu

## Slide 2
Overview
River restoration techniques
  In-stream restoration
  Channel modification techniques
Large wood placement
Case study Crab Creek/Green River
Summary

## Slide 3
RIVER RESTORATION
TECHNIQUES

## Slide 4
In-Stream Techniques
In stream habitat restoration includes:
  Addition of spawning gravels
  Boulder placement
Nutrient Enrichment:
  Addition of inorganic N and P
  Distribution of salmon carcasses

## Slide 5
In-Stream Techniques
Artificial Structures
  Weirs (bank protection, channel stability)
  Wire Gabions (bank stabilization, silt filtration)

## Slide 6
Example of boulder placement to create channel roughness

## Slide 7
Example artificial structures- porous weir

## Slide 8
Example artificial structures- rip rap gabion
Rip Rap

## Slide 9
Channel Modification
Techniques
Cross section change
Bank reconstruction
Altering channel profile
Enhancing sediment transport

## Slide 10
LARGE WOOD PLACEMENT

## Slide 11
Examples of large wood in channels

## Slide 12
Large Wood Placement
Fundamentals
Addresses a deficiency of habitat
Natural channel-forming processes
Short term solution
Provides habitat while natural processes are restored
Promotes channel complexity & roughness

## Slide 13
Large Wood Placement
Benefits
Retains organics
Absorbs the force of high flows
Reduces bank erosion
Recruits additional wood
Recruits, sorts, and retains spawning gravel
Provides movement pathways for wildlife

## Slide 14
Example of LWD creating channel complexity
Stage 1
Stage 2
Stage 3

## Slide 15
PLACED LARGE WOOD

## Slide 16
Placed Large Wood
Deliberate placement of wood in streams
  Form discrete LW, logjams structures
  Create habitat directly
  Use natural processes that scour and deposit
  Re-establish natural LW loading volumes and distributions

## Slide 17
LWD placement techniques

## Slide 18
Large wood structure example: Constructed Log Jam

## Slide 19
TRAPPING MOBILE WOOD

## Slide 20
Example of how large wood creates habitat
Floodplain

## Slide 21
End result of trapping mobile wood

## Slide 22
CASE STUDIES:
CRAB CREEK / GREEN RIVER

## Slide 23
Crab Creek

## Slide 24
Project Overview
Project length 2002-2007
  Objective: To increase Coho salmon populations
  Primary restoration method, LWD
  Crab Creek received 172 trees
  Green River received 248 trees
  Form habitat using wooden debris

## Slide 25
Crab Creek Results
Change | Change observed
Pool depth | Modest to undetectable changes have occurred in residual pool depth.
Pool surface area | The number of pools having a residual depth > 1m increased slightly as did their surface area.
Spawning Gravel | observed to have a 93% increase, pre-project year to the most recent post-project year.
Habitat formation | Channel roughness was also seen to increase, as a result.

## Slide 26
Crab Creek (Cont.)
Change | Change observed
Habitat area | Side channel habitat has increased post-treatment, providing almost four times in area.
Large wood Pre-project + Treatment = 742 Post-project (2006) = 915 | The post-project wood counts of both years exceed the sum of pre-project and treatment wood. With 173 species of Native wood recruited.

## Slide 27
Green River

## Slide 28
Green River Results
Change | Change observed
Main stream habitat | mainstem primary channel habitat units increased from 158 pre-treatment to 202 post- treatment.
Scour Pools | number of scour pools increased from (83 to 119)
Riffle habitats | Riffle habitats increased from (63 to 79)
Winter Coho carrying capacity | The winter abundance has exhibited a steady increase with no indication of a ceiling in capacity.

## Slide 29
DISCUSSION
Most applied techniques are short term
Outcomes not always certain
Rarely seen to have immediate results
Project may essentially disturb river system

## Slide 30
Summary
River restoration techniques
  In-stream restoration
  Channel modification techniques
Large wood debris (trapped and placed)
Uses natural materials and processes
Habitat forming
Creates channel complexity
River Restoration is “Habit” Forming